## Slide 1: PLASTICS POLLUTION AND CLIMATE CHANGE
IN 00.41: Climate Change Challenges and Responses
Additional Information / Reading Materials
Asian Institute of Technology
January 2021

## Slide 2: Key Questions
What is the plastic pollution issue? Why and how is it linked to the climate change issue?
What is the current plastic demand? What is happening to the plastic waste?
How can we minimize the plastic pollution issue and mitigate climate change?
This lecture focuses on the understating of the plastic pollution issue through the lens of climate change at large. It discusses the interlinkages, the demand and the waste generation of plastics and finally outlines a way forward to mitigate plastic pollution and climate change.

## Slide 3: Brief Outline
Status of plastic production and use
Role of plastic pollution in climate change
Plastic waste management as an option to mitigate climate change impact
Way forward

## Slide 5: Plastic Pollution
Not only an Marine Pollution Issue
But also a climate issue

## Slide 6: Why plastics are also climate change issues?
Petrochemicals: chemicals derived from fossil fuels and used to make plastics, fertilizers, synthetic rubber and other products are becoming a huge driver of global oil and natural gas use.
They will account for more than a third of the global growth of oil demand by 2030 and nearly half by 2050 — more than trucks, aviation and shipping combined.
Polyethylene — the type of plastic in grocery bags, and the most produced and discarded plastic globally — is an abundant emitter of both methane and ethylene (greenhouse gases)
Plastics reduce oceans ability to absorb GHGs: interfering with microscopic plants (phyto-planktons) and animals (zooplanktons) metabolism, reproductive abilities and survival, and therefore their potential ability to act as a carbon sink. These organisms are likely to consume petrochemicals and plastics bits

## Slide 7: Data and Information on Plastics
Half of all plastics ever manufactured have been made in the last 15 years.
Production increased exponentially, from 2.3 million tons in 1950 to 448 million tons by 2015. Production is expected to double by 2050.
Every year, about 8 million tons of plastic waste escapes into the oceans from coastal nations. That’s the equivalent of setting five garbage bags full of trash on every foot of coastline around the world.
Plastics often contain additives making them stronger, more flexible, and durable. But many of these additives can extend the life of products if they become litter, with some estimates ranging to at least 400 years to break down.
https://www.nationalgeographic.com/environment/habitats/plastic-pollution/

## Slide 8: Plastic Production and Demand
Production
Demand Projection
China, Developing Asia, Middle East and Africa will see surging demands in this century.

## Slide 9: Plastic Production and Waste Generation by Industrial Sector
Production
Waste Generation
Packaging sector largest contributor

## Slide 10: Plastic Production and Industry
Plastic production and use (estimated) will occur at the rate of 3.8%/year through 2030 (WEF)
Rate of growth will drop to 3.5%/year from 2030 through 2050.
The production capacity for ethylene and propylene (important plastic feed stocks) would increase by 33–36% by 2025 (CIEL, 2017)
American Chemistry Council reported a total of $164 billion of investment in 260 new or expanded production facilities for petrochemicals (calculating from a 2010 base-line).
By September 2018: total investments of over $200 billion in more than 330 new or expanded facilities.
All these data reflects the increasing tendency of GHGs

## Slide 11: How plastics contribute to climate change?

## Slide 12: GHG and Plastic Life Cycle
https://www.ncel.net/2020/03/05/plastic-pollution-and-public-health-a-toxic-relationship/
GHGs are emitted at each of each stage of the plastic lifecycle:
  fossil fuel extraction and transport,
  plastic refining and manufacture,
  managing plastic waste, and
  plastic’s ongoing impact once it reaches our oceans, waterways, and landscape.

## Slide 13: Emissions from the Plastic Lifecycle
In 2019, the production and incineration of plastic approximately added more than 850 million metric tons of GHG to the atmosphere: equal to the emissions from 189 five- hundred-megawatt coal power plants.
On average, the production of one ton of plastic resin will emit 1.89 Mt CO2e.

## Slide 14: Extraction and Transport
Sources include direct emissions, like methane leakage and flaring, emissions from fuel combustion and energy consumption in the process of drilling for oil or gas, and emissions caused by land disturbance when forests and fields are cleared for well pads and pipelines.
In US in 2015, emissions from fossil fuel (largely fracked gas) extraction and transport attributed to plastic production were at least 9.5–10.5 million metric tons of CO2 equivalents (CO2e) per year.
Outside the US, where oil is the primary feedstock for plastic production, approximately 108 million metric tons of CO2e per year are attributable to plastic production, mainly from extraction and refining.
Hamilton, L.A., Feit, S., Muffett, C., Kelso, M., Rubright, S.M., Bernhardt, C., Schaeffer, E., Moon, D., Morris, J. and Labbé-Bellas, R., 2019. Plastic & Climate: The Hidden Costs of a Plastic Planet. Center for International Environmental Law (CIEL).

## Slide 15: Refining and Manufacture
Plastic refining is among the most greenhouse gas intensive industries in the manufacturing sector and fastest growing.
The manufacture of plastic is both energy intense and emissions intensive producing significant emissions through the cracking of alkanes into olefins, the polymerization and plasticization of olefins into plastic resins, and other chemical refining processes.
In 2015, 24 ethylene facilities in the US produced 17.5 million metric tons of CO2e, emitting as much CO2 as 3.8 million passenger vehicles.
Globally in 2015, emissions from cracking to produce ethylene were 184.3–213.0 million metric tons of CO2e, as much as 45 million passenger vehicles driven for one year.
Hamilton, L.A., Feit, S., Muffett, C., Kelso, M., Rubright, S.M., Bernhardt, C., Schaeffer, E., Moon, D., Morris, J. and Labbé-Bellas, R., 2019. Plastic & Climate: The Hidden Costs of a Plastic Planet. Center for International Environmental Law (CIEL).

## Slide 16: Plastic Waste Management

## Slide 17: Global Mismanaged Plastic
Our Region…East Asia and Pacific is the worst!
South Asia is at 11%

## Slide 18: Plastic Waste Management
Plastic is primarily landfilled, recycled, or incinerated: each of which emit GHGs.
Landfilling emits the least GHGs on an absolute level, although it presents significant other risks.
Recycling has a moderate emissions profile but displaces new virgin plastic on the market, making it beneficial from an emissions perspective.
Incineration is responsible for extremely high emissions
Globally, the use of incineration in plastic waste management is growing dramatically
US emissions from plastic incineration in 2015 are estimated at 5.9 million metric tons of CO2e.
For plastic packaging, which represents 40% of plastic demand, global emissions from incineration of this particular type of plastic waste totaled 16 million metric tons of CO2e in 2015.
Hamilton, L.A., Feit, S., Muffett, C., Kelso, M., Rubright, S.M., Bernhardt, C., Schaeffer, E., Moon, D., Morris, J. and Labbé-Bellas, R., 2019. Plastic & Climate: The Hidden Costs of a Plastic Planet. Center for International Environmental Law (CIEL).

## Slide 19: Global Plastic Waste Disposal
Most Plastics are simply discarded
Global
US

## Slide 20: Climate Impacts of Plastic Packaging and Waste Disposal Options (kg CO2e/metric ton)

## Slide 21: Plastic Recycling and Incineration
Plastic recycling is less profitable and require high government subsidies: due to high costs of recycling steps (collection, transportation, processing, remanufacturing), low commercial value of recycled plastic, and low cost of virgin material
One Mt of plastic packaging = 79 percent combustible carbon content, which would release 790 kg of carbon(2.9 Mt of CO2), into the atmosphere (average estimate).
Climate impact of plastic waste incineration in the US: equivalent to 1.26 million passenger vehicles driven for one year, or more than half billion gallons of gasoline consumed

## Slide 22: Path to Zero Waste
Zero waste: systemic approach to waste prevention and reduction
Include decentralized separated collection, sorting and reuse of waste
Also include an iterative evaluation process- support communities to assess the waste stream and implement policies to reduce the production and consumption of materials which as difficult to recover. Example: bans on single-use plastic items.
Aim to return all materials to the community as a resource without being processed in incinerators or landfilled
Climate benefits of zero waste : non-essential plastic packaging would be removed resulting in no emissions from downstream waste management.

## Slide 25: Plastic and Climate Change: The hidden Cost of a Plastics Planet

## Slide 26: Hidden Costs of Plastics
There are an estimated 270,000 tons of plastic floating through the world’s seas where it threatens 700 marine species with its presence
Most of the deaths to animals are caused by entanglement or starvation
S.C. Gall, R.C. Thompson,The impact of debris on marine life,Marine Pollution Bulletin,
Volume 92, Issues 1–2,2015,Pages 170-179,ISSN 0025-326X, https://doi.org/10.1016/j.marpolbul.2014.12.041.
Plastics have also been found to have blocked digestive tracts or pierced organs, causing death

## Slide 27: Increased GHGs and decreased carbon sinks
Plastics at the ocean’s surface continually releases methane and other GHGs, and these emissions increase as plastic breaks down further
Plastic on the coastlines, riverbanks, and landscapes releases GHGs at an even higher rate.
Microplastic in the oceans may also interfere with the ocean’s capacity to absorb and sequester carbon dioxide.
Earth’s oceans have absorbed 20–40 percent of all anthropogenic carbon emitted since the dawn of the industrial era.
Plastic pollution can reduce the ability of phytoplankton to fix carbon through photosynthesis.
Plastic pollution can reduce the metabolic rates, reproductive success, and survival of zooplankton that transfer the carbon to the deep ocean.
https://www.cawrecycles.org/recycling-news/to2ro7f8g2vz8f66nnddlbb895oshk
https://www.cawrecycles.org/recycling-news/to2ro7f8g2vz8f66nnddlbb895oshk

## Slide 29: 9 Reasons to Refuse Single Use Plastic Bags

## Slide 30: Annual plastics emissions (2015 estimate)

## Slide 31: Annual Projections to 2050 and beyond
If plastic production and use grow as currently planned, by 2030, these emissions could reach 1.34 gigatons per year: equivalent to the emissions released by more than 295 new 500-megawatt coal-fired power plants.
By 2050, GHGs emissions from plastic could reach over 56 gigatons: 10–13% of the entire remaining carbon budget
By 2100 it will emit 260 billion tonnes, more than half of the carbon budget. Those are emission from production, transportation, incineration, but there are also releases of methane and effects on phytoplanktons

## Slide 32: Life cycle Plastics emissions to mitigation and carbon budget targets
Current emissions projections for the plastic lifecycle are inconsistent with meeting the 1.5°C temperature target.
Even if growth slows after 2030, plastic production and incineration could emit 2.8 gigatons of CO2 per year by 2050, releasing as much emissions as 615 five-hundred-megawatt coal plants.
To avoid exceeding the 1.5°C target, aggregate global greenhouse emissions must stay within a remaining (and quickly declining) carbon budget of 420–570 gigatons of carbon
Of the 800 Gt CO2e carbon budget for energy and industry sectors through 2100 under a 2°C scenario, Material Economics allocates 300 Gt for industry.
Governments must seek additional, rapid emissions cuts.
Emissions cuts from reducing the production and consumption of plastic will also help to address other important environmental and social issues

## Slide 33: Way Forward
Using only zero-carbon energy sources, such as wind and solar, in the manufacturing phase would decrease overall emissions by 50%.
Thinking critically about the materials that will replace plastics: reuse the bags as many times as possible (example: paper or cotton bags for shopping)
Reducing waste, retaining materials by refurbishing or remanufacturing, and recycling.
In circular business model, carbon dioxide emissions would decrease by 62 million metric tons per year (CIEL)
Introducing regulation for banning single use plastics
Community awareness for controlling plastic wastes

## Slide 34: Way Forward
Plastics is not just an oceans issue but it’s also a climate issue, and also appears to be reducing the oceans ability to absorb GHGs
Plastics will account for more than 1/3 of the global growth of oil demand by 2030 and nearly ½ by 2050– more than trucks, aviation, and shipping combined
By 2050 , the GHG emissions from plastics could reach over 56 Gt or 10-13% of the entire remaining carbon budget
Current GHG emissions from Plastics Lifecycles threaten our ability to meet Global Climate Targets
Four industrial sectors- steel, plastics ,cement, and aluminum account for 3/$ of the total emissions by the industrial sector (total from industrial sector about 40 % of the global GHG emissions). Of the four sectors, PLASTICS is projected to have the largest growth in emissions under the BAU scenarios
Plastics waste management is important and should move towards Zero Waste Paths in the long run and looking positive .

## Slide 35: References
Plastic & Climate The Hidden Costs of a Plastic Planet https://www.ciel.org/plasticandclimate/
https://www.greenbiz.com/article/why-plastics-are-also-climate-issue
https://yaleclimatemediaforum.org/2019/08/how-plastics-contribute-to-climate-change/
https://www.nationalgeographic.com/environment/habitats/plastic-pollution/
https://ourworldindata.org/plastic-pollution

## Slide 36: Thank you
Contact: Dr Bindu Lohani (bnlohani@gmail.com)